## Slide 1: Computer Architecture CSE – 3521 MID-Term
Mahir Shadid (MAS)
Lecturer, Dept. of CSE, IIUC

## Slide 2: Segment - 1

## Slide 3: Computer Architecture Basics
Computer Architecture: Design and Organization of computer components to optimize performance.
Computer Organization: How a computer’s hardware components work together to execute programs. It includes memory, CPU, and input/output operations.
Abacus: An ancient counting tool used for basic arithmetic operations, considered one of the first computing devices.

## Slide 4: Computer Architecture Basics
History: Five generations:
  First Gen (1940-1956): Computers used Vacuum Tube containing Cathode (electron emission), Anode (electron collection) and Grid (switch).
    Example: ENIAC (Electronic Numerical Integrator and Computer) - The first general-purpose electronic computer (built in 1945). It was huge and used vacuum tubes.
  Second Gen (1956-1963): Computers used Transistors (acted as switch)which were smaller and faster containing Emitter, Base and Collector.
  Third Gen (1964-1971): ICs (Integrated Circuits) created on Silicon Chips, which were basically “multiple transistors”.
  Fourth Gen (1971-present): Microprocessors (thousands of transistors), contains CPU, Memory Units etc. Also known as “system on chips”.
  Fifth Gen (Future): AI and quantum computing.

## Slide 5: Computer Architecture Basics
Types of Computer Architecture:
  Von Neumann (Recent computers).
  Harvard (embedded-systems).
  RISC (Reduced Instruction Set Computer): used in ARM-based devices.
  CISC (Complex Instruction Set Computer): used in x86-based devices.
Von Neumann Architecture: Components:
  CPU (Central Processing Unit): An electronic circuit (microprocessor) that executes instructions.
  Control Unit: Controls the operations of ALU (Arithmetic Logic Unit), memory and I/O. Manages data flow.
  Registers (High speed storage cells).
  Memory Unit: primarily consists of RAM.

## Slide 6: Von Neumann Architecture
PC (Program counter): holds the address of next instruction.
AC (Accumulator): ALU operations occur here.
MAR (Mem. Address Register): stores the address of memory to be accessed (either for fetching an instruction or reading/writing data).
MDR (Mem. Data Register): stores the data of an instruction.
CIR (Current Instruction Register): holds the current instruction.

## Slide 7: Von Neumann Architecture
Advantages of Von Neumann:
  Simple & Cost-Effective: Uses a single memory for both data & instructions, making it easier and cheaper to build.
  Flexible: Can execute different programs by just loading new instructions into memory.
  Efficient Use of Memory: Same memory can store both code and data dynamically.
  Widespread Usage: Most modern computers use this design, making it well-supported.
Disadvantages of Von Neumann Architecture:
  Von Neumann Bottleneck: The single memory bus limits the speed, as instructions and data share the same path.
  Slower Execution: Fetching data and instructions sequentially can slow down performance.
  Risk of Overwriting: Since instructions and data share the same memory, a bug can accidentally modify the program.

## Slide 8: System bus
For connecting the components in a computer architecture we use a system bus (set of parallel wires). System Bus consists of:
  Data Bus: bi-directional (two-way data flow), used to carry data and instruction. Transmits data between CPU, Memory and I/O.
  Address Bus: unidirectional (one-way), carries memory location where data needs to be sent. Carries address from CPU to RAM and I/O.
  Control Bus: bi-directional, used to carry control signals (Read, write, interrupt, reset).

## Slide 9: RISC (Reduced Instruction Set Computer) Architecture
Small, highly optimized instruction set that executes in a single clock cycle. Instructions set in RISC are fixed-length (usually 32-bits). RISC enables pipelining (executing multiple instructions simultaneously in different stages of the instruction cycle).
Example: Multiplying 2 values:
  LOAD R1, A ; Load value A into register R1
  LOAD R2, B ; Load value B into register R2
  MUL R3, R1, R2 ; Multiply R1 and R2, store in R3
  STORE R3, C ; Store result in memory location C
Few, simple instructions: Each instruction takes one clock cycle.
Fixed instruction size: Easy to decode and execute.
More registers: Uses registers for computations instead of memory.
More lines of code: Simple instructions mean more instructions are needed to complete a task.
Less complex hardware: Easier to design and optimize.
Used in modern processors: ARM, MIPS.

## Slide 10: CISC (Complex Instruction Set Computer) Architecture:
Single but complex instruction set, can perform multiple operations, can take multiple clock cycles, has variable-length (8-120 bits).
Example: Multiplying 2 values:
  MUL A, B, C ; Multiply values at memory locations B and C, store in A
Many complex instructions: One instruction can do multiple tasks.
Variable instruction size: Harder to decode and execute.
More memory operations: Relies more on RAM instead of registers.
Fewer lines of code: One complex instruction does more work.
More complex hardware: Harder to design but powerful.
Used in traditional and desktop processors: Intel x86, AMD.

## Slide 11: Understanding Program Performance
Program performance: ability of a computer program to execute programs efficiently. Measured in execution time and throughput.
Execution time: time taken to complete a task. Lower, Better.
Execution time
  = CPU clock cycles for a program (CPI) * clock cycle time (Using Clock Cycle Time)
  = CPU clock cycles for a program / Clock rate (General Formula)
  = Instruction Count x CPI / Clock Rate (Using Instruction Count & CPI)
Throughput: number of tasks completed in a given time. Higher, Better.
Speed up ratio: execution time on slow device/execution time on fast device.

## Slide 12: Understanding Program Performance
CPU clock cycle: It determines how fast the processor executes instructions.
Response time: The total time from when a user gives an input until the system gives the output.
CPU Time: The actual time the CPU spends processing a program (excluding time spent waiting for input/output).
System CPU Time: The time the CPU spends on system-level operations (like managing memory, handling I/O), not just user programs.
Relative Performance: A comparison of how fast one computer or processor is compared to another. Higher relative performance means a faster system.
CPI (Cycles Per Instruction): The average number of clock cycles needed to execute one instruction. Lower CPI means faster performance.

## Slide 13: Understanding Program Performance
Key factors that affects computer performance:
  Clock Speed (expressed in GHz, instructions processed per second) - 4GHz performs better than 3GHz.
  Instruction count (fewer, faster).
  CPI (how many cycles a CPU takes per instruction).

## Slide 14: Amdahl’s Law
Determines maximum possible performance gain by improving one part of the system.
Calculated by, Speed Up = 1 / (1-p) + (p/s)
  P = fraction of improved task
  S = speed up factor / Number of processors
Example: if 50% of a task is optimized, and speed up is 2x, overall speed up would be,
  1 / (1-0.5) + (0.5/2) = 1.33x

## Slide 15: MIPS (Millions Instructions Per Second) - 32 bits
A metric used to measure the performance of a computer's processor. It refers to how many millions of instructions a processor can execute in one second.
IPS = Instruction Count / Execution time
MIPS = (Instruction Count / Execution time) x 10^6
MIPS = (Clock rate / CPI) x 10^6
MIPS = Total Instruction / Execution Time
Example:
Device | Instruction Counts in Billions |  | 
 | A | B | C
Compiler 1 | 4 | 2 | 3
Compiler 2 | 10 | 5 | 4

## Slide 16: MIPS (Millions Instructions Per Second) - 32 bits
Device | Instruction Counts in Billions |  | 
 | A | B | C
Compiler 1 | 4 | 2 | 3
Compiler 2 | 10 | 5 | 4
Instruction Class | CPI
A | 1
B | 2
C | 3
If the computer’s clock rate is 5 GHz, which code sequence will execute faster according to execution time?

## Slide 17: MIPS (Millions Instructions Per Second) - 32 bits
  Compiler 1’s total cycle = (4 x 1) + (2 x 2) + (3 x 3) = 17 billion cycles
  Compiler 2’s total cycle = (10 x 1) + (5 x 2) + (4 x 3) = 32 billion cycles
Execution time = Total cycle / clock rate
  Compiler 1’s execution time = 17 / 5 = 3.4 s. (5 GHz is given)
  Compiler 2’s execution time = 32 / 5 = 6.4 s. (5 GHz is given)
MIPS = Total instruction / execution time
  Complier 1’s MIPS = (4+2+3) = (9 billion x 1000) = 9000 millions instructions / 3.4s = 9000 / 3.4 = 2647 MIPS.
  Complier 2’s MIPS = (10+5+4) = (19 billion x 1000) = 19000 millions instructions / 6.4s = 19000 / 6.4 = 2969 MIPS.
Ans: This shows Compiler 2 has a higher MIPS but slower execution time, a classic paradox of MIPS as a performance metric.
Total Cycles (Total CPI) = ∑(Instruction count × Cycles per instruction)

## Slide 18: MIPS (Millions Instructions Per Second) - 32 bits
Now try:
  Suppose we have two implementations of the same instruction set architecture. Computer1 has a CPI of 3.0 and a clock cycle time of 300 ps for some programs, and Computer2 has a CPI of 4.0 and a clock cycle time of 150 ps for the same programs. Which computer is faster for this program and by how much?

## Slide 19: MIPS (Millions Instructions Per Second) - 32 bits
Suppose we have two implementations of the same instruction set architecture. Computer1 has a CPI of 3.0 and a clock cycle time of 300 ps for some programs, and Computer2 has a CPI of 4.0 and a clock cycle time of 150 ps for the same programs. Which computer is faster for this program and by how much?
Which one is faster?
  Execution time = CPI x Clock cycle time
  Computer1 = 3 x 300 = 900ps
  Computer2 = 4 x 150 = 600ps (Faster)
How much faster?
  Speed up ratio = execution time of slow device / execution time of fast device = 900/600 = 1.5.
  Which means Computer2 is 1.5x faster.

## Slide 20: MIPS (Millions Instructions Per Second) - 32 bits
What is CPU clock cycle and clock rate? UNIX time command is given 40.4u 10.5s 2:50. Calculate the percentage according to total elapsed time.
Given:
  User CPU time = 40.4 s
  System CPU time = 10.5 s
  Total elapsed time = 2:50 = 2×60 + 50 = 170 seconds
The question says percentage according to total elapsed time. Usually, this means:
  Percentage = x 100
Total CPU time = 40.4+10.5 = 50.9 s

## Slide 21: MIPS (Millions Instructions Per Second) - 32 bits
  Percentage = x 100 = 29.94% (ANS)
MIPS does not always directly indicate performance because:
  Different CPI values: A machine with a high MIPS value may have a low CPI, but it does not necessarily mean it completes tasks faster.
  Instruction Set Differences: Some architectures may execute instructions in fewer cycles but at a lower MIPS rate.
  Clock Speed Impact: A higher clock speed can lead to a higher MIPS, but actual execution time may still be longer.
Thus, a machine with higher MIPS does not always execute a program faster if CPI is also higher.

## Slide 22: Segment-2

## Slide 23: Instruction Set Architecture
ISA (Instruction Set Architecture): Defines the types of instructions supported by a processor.
Types:
  Stack-based ISA: Uses a stack for all operations (push/pop). No direct access to registers. Example: JVM (Java Virtual Machine).
  Accumulator-based ISA: Uses a single accumulator register for most operations. Simple but results in more memory access. Example: Intel 8008, 8051 Microcontrollers.
  Register-based ISA: Uses multiple registers for operations instead of a stack or accumulator. Faster than stack or accumulator-based architectures. Example: Intel x86.

## Slide 24: Instruction Set Architecture
Instruction Set: Collection of machine language instruction. 5 types:
  Arithmetic: add, sub, mul, div.
  Logical: AND, OR, NOT.
  Data Transfer: MOV, LOAD, STORE.
  Control Flow: JUMP, CALL, RETURN.
  I/O

## Slide 25: Instruction Set Architecture
Instruction Access methods: Instruction access refers to how the CPU fetches and retrieves instructions from memory before executing them. The CPU follows the fetch-decode-execute cycle to process each instruction.
  Sequential Access: CPU fetches instructions one after another in a sequence. After executing an instruction, the PC is incremented to point to the next instruction.
  Direct Access: The instruction address is directly specified in the instruction itself. Used in branching and jumping instructions. Example: JMP 0x200 ; Jump to memory location 0x200.
  Indirect Access: The instruction contains an address that points to another memory location where the actual instruction is stored. Example: JMP [0x200] ; Fetch address from location 0x200 and jump there.

## Slide 26: Instruction Set Architecture
Data Access Methods: Data access refers to how the CPU retrieves and stores data in memory or registers during instruction execution. Different addressing modes determine how the data is accessed.
  Register Addressing: data (operand) is stored in a CPU register. Ex: ADD R1, R2, R3 ; R1 = R2 + R3.
  Immediate Addressing: data (operand) is part of the instruction itself. Ex: ADDI R1, R2, 10 ; R1 = R2 + 10.
  Direct Addressing: The instruction specifies the exact memory address where the operand is located. Ex: LOAD R1, 0x2000 ; Load value from memory address 0x2000 into R1.
  Indirect Addressing: The instruction provides a memory location that stores another address where the actual operand is located. Ex: LOAD R1, [0x2000] ; Fetch address stored at 0x2000, then load value from that address.
  Indexed Addressing: A base address is combined with an offset stored in an index register. Ex: LOAD R1, 100(R2) ; Load value from memory address (R2 + 100) into R1.

## Slide 27: Stored-Program Concept
The Stored-Program Concept is a fundamental principle of modern computing, introduced by John von Neumann. This concept is the basis for the Von Neumann Architecture, where instructions and data are stored in the same memory and accessed via the same data bus. Programs can be modified during execution.
Consider a simple program that adds two numbers stored in memory:
Step-by-Step Execution:
    Program and data are loaded into memory: CPU fetches both instructions and operands from RAM.
    CPU Fetches and Decodes the Instruction: The first instruction (e.g., LOAD A) is fetched and sent to the Instruction Register (IR). The Program Counter (PC) is updated to point to the next instruction.
    Instruction Execution: The instruction is executed (e.g., the addition is performed in the ALU).
    Store Result in Memory: The result is stored back in RAM for later use.

## Slide 28: Operations of the Computer Hardware
Computer hardware operations follow the fetch-decode-execute cycle:
  Fetch: The CPU retrieves an instruction from memory.
  Decode: The instruction is interpreted by the control unit.
  Execute: The ALU (Arithmetic Logic Unit) or other components perform the operation.
  Write Back: The result is stored in a register or memory.

## Slide 29: Operands of the computer hardware
Operands are the values or data on which instructions operate. They can be stored in:
  Registers: Fastest storage location within the CPU.
  Memory: Slower access, requires address calculation.
  I/O Devices: External inputs such as keyboard, mouse, or sensors.
Design Principles of Computer Hardware:
  Simplicity Favors Regularity: Using uniform instruction formats.
  Smaller is Faster: Reducing instruction complexity speeds up execution.
  Make the Common Case Fast: Optimizing frequent operations.

## Slide 30: Representation of Instructions in the Computer
Instructions are stored in binary format. The MIPS instruction format consists of:
  Opcode: Specifies the operation (ADD, LOAD, etc).
  Operands: Register/memory locations involved.
  Addressing Mode: Defines how to locate data.
Instructions for Decision Making: Conditional and branching instructions alter the program flow based on conditions.
  Branching:
    BEQ (Branch if Equal): Jumps to a label if two registers are equal.
    BNE (Branch if Not Equal): Jumps if they are different.
  Jumping:
    J (Jump): Unconditionally jumps to a new instruction address.

## Slide 31: MIPS Addressing for 32-bit Immediate and Addresses
MIPS uses different addressing modes for memory access and instruction execution.
  Immediate Addressing: The operand is directly in the instruction.
  Register Addressing: Uses register values.
  Base (Displacement) Addressing: Adds an immediate offset to a base register.
  PC-Relative Addressing: Used in branch instructions. The offset is added to the program counter.
  Jump Addressing: Used in J and JAL instructions to specify an absolute jump address.

## Slide 32: Instruction formats/MIPS Addressing Modes
Instruction formats define the structure of machine-level instructions, specifying how operands, opcodes, and addressing modes are arranged. There are three primary instruction formats:
R-Type (Register-Type) Format: Used for register-to-register operations (mostly arithmetic and logic operations).
  Fields (Total 32 bits): opcode (6 bits) | rs (5 bits) | rt (5 bits) | rd (5 bits) | shamt (5 bits) | funct (6 bits)
    Opcode (6 bits) – Operation code
    rs (5 bits) – Source register
    rt (5 bits) – Target register
    rd (5 bits) – Destination register
    shamt (5 bits) – Shift amount (used for shift operations like sll, srl, etc.)
    funct (6 bits) – Function code for ALU operations

## Slide 33: Instruction formats/MIPS Addressing Modes
I-Type (Immediate-Type) Format: Used for operations with an immediate value or memory access instructions. Immediate values or memory addresses are directly provided in the instruction.
  Fields (32 bits): opcode (6 bits) | rs (5 bits) | rt (5 bits) | offset (16 bits)
    Opcode (6 bits) – Operation code
    rs (5 bits) – Source register
    rt (5 bits) – Destination register
    Immediate (16 bits) – Constant or memory offset

## Slide 34: Instruction formats/MIPS Addressing Modes
J-Type (Jump-Type) Format: Used for unconditional jumps (changing execution flow). Contains only an address to jump to.
  Fields (32 bits): Opcode (6 bits) | Target Address (26 bits)
    Opcode (6 bits) – Operation code
    Target Address (26 bits) – Jump destination
Two types of Opcode:
  j → Jump 2 steps ahead → 000010
  jal → Jump + Link (1 extra) → 000011

## Slide 35: MIPS register mapping
An easy way to remember the MIPS register numbers in a structured way:
  The temporary registers ($t0 to $t9) start at 8 and go up to 15 ($t0 = 8, $t1 = 9, ..., $t7 = 15), then $t8 is 24 and $t9 is 25.
  The saved registers ($s0 to $s7) start at 16 and go up to 23 ($s0 = 16, $s1 = 17, ..., $s7 = 23).
  The special purpose registers include $zero (0), $at (1), $v0 (2), $v1 (3), and the argument registers $a0 to $a3 (4 to 7).
  The kernel registers $k0 and $k1 are 26 and 27, while $gp (global pointer) is 28, $sp (stack pointer) is 29, $fp (frame pointer) is 30, and $ra (return address) is 31.

## Slide 36: MIPS register mapping
Register | MIPS register numbers
Temporary Registers ($t0 - $t7) | 8 – 15
Temporary Register $t8 | 24
Temporary Register $t9 | 25
Saved Registers $s0 - $s7 | 16 – 23
Argument Registers $a0 - $a3 | 4 - 7

## Slide 37: MIPS register mapping: Function Codes
Addition (add = 100000 = 0x20): Think of "20 means add", since it's a basic operation.
Subtraction (sub = 100010 = 0x22): It's just add but with the 2nd bit flipped (10).
Logical operations (and, or, xor, nor):
  1001XX → and, or, xor, nor follow a pattern.
  and = 100100, or = 100101, xor = 100110, nor = 100111 (incrementing last 2 bits).
Set Less Than (slt = 101010):
  Think of "10-10" (slt checks if one number is less than another).
Branching:
  Beq = 000100
  Bne = 000101

## Slide 38: MIPS register mapping: Operation Codes
Instruction | Type | Opcode (binary)
add | R | 000000
sub | R | 000000
slt | R | 000000
addi | I | 001000
lw | I | 100011
sw | I | 101011
beq | I | 000100
bne | I | 000101
j | J | 000010

## Slide 39: MIPS REGISTER MAPPING: FUNCTION CODES (R-Type)
Instruction | Type | Funct (binary)
add | R | 100000
sub | R | 100010
and | R | 100100
or | R | 100101
slt | R | 101010
sll | R | 000000
srl | R | 000010
jr | R | 001000
nor | R | 100111

## Slide 40: MIPS register mapping: EXamples
Example:
  Translate the following instruction into machine instruction:
  Add $t5, $s3, $s4
This is a R-type instruction. Thus:
  Add = 100000 (Function codes are in 6 digits binary)
  T5 = 13 = 01101 (Register mappings are 5 digits)
  S3 = 19 = 10011
  S4 = 20 = 10100
Machine instruction for R-type
  = opcode (6 bits) | rs (5 bits) | rt (5 bits) | rd (5 bits) | shamt (5 bits) | funct (6 bits)
  = 000000 (for add) | s3 | s4 | t5 | 00000 (for add) | 100000 (func code of add)
  = 000000 10011 10100 01101 00000 100000
  = 0x02746820 Hex (Ans.)

## Slide 41: MIPS register mapping: EXamples
beq $t1, $s2, 1000 (I-type problem because of direct constant)
So structure is “opcode (6 bits) | rs (5 bits) | rt (5 bits) | offset (16 bits)”
  Beq = 000100
  T1 = 9 = 01001
  s2 = 18 = 10010
  1000 = 0000001111101000
Machine instruction for I-type = 000100 01001 10010 0000001111101000 = 0x113203E8 Hex (Ans.)

## Slide 42: MIPS register mapping: EXamples
SLL (Shift Left Logical) - R-type Instruction: sll $t0, $t1, 5
Field - opcode (6) | rs (5) | rt (5) | rd (5) | shamt (5) | funct (6)
  opcode -> Operation code (always 0 for R-type) -> 000000
  Rs -> Source register (Not used in SLL) -> 00000
  Rt -> Second source register -> $t1 -> 01001
  Rd -> Destination register -> $t0 -> 01000
  Shamt -> Shift amount -> 5 -> 00101
  Funct -> Function code for SLL -> 000000
Binary Code: 000000 00000 01001 01000 00101 000000
HEX Code: 0x00094140 (Ans.)

## Slide 43: Important questions: 1
Class | CPI | Compiler A | Compiler B
A | 1 | 5 | 4
B | 2 | 2 | 3
C | 3 | 1 | 2
Assuming a 2.5 GHz clock, calculate which compiler produces faster codes? |  |  | 

## Slide 44: Important questions: 1
Class | CPI | Compiler A | Compiler B
A | 1 | 5 | 4
B | 2 | 2 | 3
C | 3 | 1 | 2
Assuming a 2.5 GHz clock, calculate which compiler produces faster codes? |  |  | 
Compiler A’s Total CPI = (5x1)+(2x2)+(1x3) = 12 CPI
Compiler B’s Total CPI = (4x1)+(3x2)+(2x3) = 16 CPI
Compiler A’s execution time = 12 / 2.5 = 0.0048 = 4.8 ms (Faster)
Compiler B’s execution time = 16 / 2.5 = 0.0064 = 6.4 ms

## Slide 45: Important questions: 2
Consider the following two CPU designs:
  CPU 1: Clock rate = 2.5 GHz, AVG. CPI = 1.6
  CPU 2: Clock rate = 2.0 GHz, AVG. CPI = 1.2
A program takes 2.2 billion instructions to execute.
  Compute the execution time on each CPU.
  Which CPU is faster and by what percentage?

## Slide 46: Important questions: 2
Consider the following two CPU designs:
  CPU 1: Clock rate = 2.5 GHz, AVG. CPI = 1.6
  CPU 2: Clock rate = 2.0 GHz, AVG. CPI = 1.2
A program takes 2.2 billion instructions to execute.
  Compute the execution time on each CPU.
  Which CPU is faster and by what percentage?
Execution time of,
  CPU 1 = ( 2.2 x 1.6 ) / 2.5 = 1.40s
  CPU 2 = ( 2.2 x 1.2 ) / 2.0 = 1.32s (Faster)
By what percentage?
  Slow / Fast = 1.40 / 1.32 = 1.060 = CPU2 is 6.0% Faster (1 – 1.060) * 100%

## Slide 47: Important questions: 3
Translate the following MIPS instructions into machine code:
  Addi t1, t2, 15
  Beq s1, s2, -8
  Lw t0, 32(sp)

## Slide 48: Segment-3

## Slide 49: Arithmetic and Logical Operations
Arithmetic Operations:
  Addition: Adds two numbers together. Example: 5 + 10 = 15
  Subtraction: Subtracts one number from another. Example: 15 - 5 = 10
Logical Operations:
  Bitwise AND (&): Sets each bit to 1 if both bits are 1. Example: 5 & 3 → 0101 & 0011 = 0001 (Result: 1)
  Bitwise OR (|): Sets each bit to 1 if one of the bits is 1. Example: 5 | 3 → 0101 | 0011 = 0111 (Result: 7)

## Slide 50: Signed and Unsigned Numbers
Unsigned numbers can only represent positive values, while signed numbers can represent both positive and negative values.
Example: Representing -5 in 4-bit Two's Complement
  Binary of +5: 0101
  One's Complement: Invert all bits → 1010
  Two's Complement: Add 1 → 1011
  Signed interpretation: -5, Unsigned interpretation: 11

## Slide 51: Number Conversion and Representation
Conversion between different numerical systems (binary, decimal, hexadecimal) and representation in computer memory.
Example: Converting 13 from Decimal to Binary:
  Division by 2 Method:
    13 ÷ 2 = 6, remainder = 1
    6 ÷ 2 = 3, remainder = 0
    3 ÷ 2 = 1, remainder = 1
    1 ÷ 2 = 0, remainder = 1
    Read remainders bottom to top:
    13 (Decimal) = 1101 (Binary)

## Slide 52: First Version of Multiplication Algorithm
Steps | Mutiplicand | Multiplier | Product
Init | 0011 | 0010 0010 | 0000 0000
2 3 | 0110 0110 | 0010 0010 0010 0001 | 0000 0000 0000 0000
1a 2 3 | 0110 1100 1100 | 0010 0001 0010 0001 0010 0000 | 0000 0110 0000 0110 0000 0110
 |  |  | 110 = 6 (ANS)
Multiply 3 x 2 ?
2 = 0010
3 = 0011

## Slide 53: Second Version of Multiplication Algorithm
Steps | Mutiplicand | Multiplier | Product
Init | 0011 | 0010 0010 | 0000 0000
2 3 |  | 0010 0010 0010 0001 | 0000 0000 0000 0000
1a 2 3 |  | 0010 0001 0010 0001 0010 0000 | 0011 0000 0001 1000 0001 1000
2 3 |  | 0010 0000 0010 0000 | 0000 1100 0000 1100
2 3 |  | 0010 0000 0010 0000 | 0000 0110 0000 0110 = 6 (ANS)
Multiply 3 x 2 ?
2 = 0010
3 = 0011

## Slide 54: First-second Version of Multiplication Algorithm: Example
In an ancient village, people did not know the “x” multiplication symbol. Instead, they only knew how to add numbers.
Suppose a farmer wants to calculate how many mangoes he has in total. He has 7 baskets, and each basket contains 5 mangoes. Since he cannot multiply directly, he decides to use the first and second version of multiplication algorithm to test both work or not.
Write down the step-by-step addition process to find the total number of mangoes.

## Slide 55: FINAL (REFINED) Version of Multiplication Algorithm
Steps | Mutiplicand | Product0 | Product
Init | 0011 | 0000 0010 | 0000 0010
2 |  | 0000 0010 | 0000 0001
1a 2 |  | 0000 0010 | 0011 0001 0001 1000
2 |  | 0000 0010 | 0000 1100
2 |  |  | 0000 0110 = 6 (ANS)
Multiply 3 x 2 ?
2 = 0010
3 = 0011

## Slide 56: First and Final Version of the Division Algorithm

## Slide 57: Resources for the algorithms
First Version of Multiplication Algorithm
Final Version of the Multiplication Algorithm
First Version of the Division Algorithm
Final Version of the Division Algorithm
Click on the titles to redirect to the resources.

## Slide 58: Floating Point Representation
Operations on real numbers, using formats like IEEE 754 to represent large/small decimal numbers.
Single and Double precision of IEEE 754:

## Slide 59: Floating Point Representation
Sign Bit
  The sign bit determines whether the number is positive or negative.
  1 bit is allocated for the sign.
  If the sign bit is 0, the number is positive.
  If the sign bit is 1, the number is negative.
Exponent
  The exponent determines the power of 2 to which the mantissa is raised.
  It is stored using biased notation:
    Single precision (32-bit): 8-bit exponent, bias = 127.
    Double precision (64-bit): 11-bit exponent, bias = 1023.
The exponent value is stored as: Exponent = Actual exponent + Bias

## Slide 60: Floating Point Representation
Mantissa (Fraction)
  The mantissa (or fraction) represents the significant part of the number.
  In IEEE 754, we use normalized representation, meaning the leading 1 is implied and not stored.
  Only the fractional part after the leading 1 is stored

## Slide 61: Floating Point Representation: Example
Show the IEEE 754 binary representation of the number –0.375₁₀ in single and double precision.
Step-1: Convert 0.375 to binary:
So, we got 0.011 in binary of 0.375.
Mul by 2 |  | Integer part
0.375 * 2 | 0.75 | 0
0.75 * 2 | 1.5 | 1
0.5 * 2 | 1.0 | 1

## Slide 62: Floating Point Representation: Example
Step-2: Normalize the Binary:
  To normalize we use implicit normalization for accuracy:
  Format: 1.xxxx * 10 ^ n
  For 0.011, it will be 1.1 * 10 ^ -2.
Step-3: IEEE 754 Single Precision Representation (32-bit):
IEEE 754 single precision consists of:
  1 bit for the sign
  8 bits for the exponent
  23 bits for the mantissa (fractional part after 1.)

## Slide 63: Floating Point Representation: Example
Sign Bit (1 bit): Since the number (-0.375) is negative, the sign bit = 1.
Exponent (8 bits): IEEE 754 uses a biased exponent with a bias of 127:
  Exponent = Actual exponent + Bias = −2 + 127 = 125.
  Convert 125​ to binary: 125 = 01111101 = 01111101 ​= 01111101.
  So, the 8-bit exponent = 01111101.
Mantissa (23 bits): We take the fractional part from step-2 = 1.1 (drop the leading 1.), so: 1000000……
Final IEEE 754 Single Precision Representation:
  1 01111101 10000000000000000000000
Binary: 1011 1110 1100 0000 0000 0000 0000 0000
Hexadecimal: 0xBE800000

## Slide 64: Floating Point Representation: Example
Step-4: IEEE 754 Double Precision Representation (64-bit):
IEEE 754 double precision consists of:
  1 bit for the sign
  11 bits for the exponent
  52 bits for the mantissa
Sign Bit (1 bit): Since the number is negative, the sign bit = 1.
Exponent (11 bits): IEEE 754 double precision uses a bias of 1023:
  Exponent = Actual exponent + Bias = −2 + 1023 = 1021.
  Convert 1021 to binary: 1021 = 01111111011.
  So, the 11-bit exponent = 01111111011.
Mantissa (52 bits): We take the fractional part 1.1 (drop the leading 1.), so: 100000….
Final IEEE 754 Double Precision Representation
  1 01111111011 1000000000000000000000000000000000000000000000000000

## Slide 65: Floating Point Representation: Example
Binary: 1011 1111 1011 1000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000
Hexadecimal: 0xBFD8000000000000 (ANS.)
Resources:
Decimal to IEEE 754
IEEE 754 to Decimal

## Slide 66: Longest Common Subsequence (LCS)
The Longest Common Subsequence (LCS) problem is a classic problem in computer science and dynamic programming. Given two sequences, the goal is to find the longest subsequence that appears in both sequences in the same order (but not necessarily consecutively).
Example: Two strings given:
  X = BACDB
  Y = BDCB

## Slide 67: Complexity Analysis of Algorithms
Complexity Analysis of Algorithms:
Complexity analysis of an algorithm determines the amount of resources (time and space) an algorithm requires based on the input size. It helps in evaluating algorithm efficiency, comparing different algorithms, and optimizing performance.
Types of Complexity Analysis
1. Time Complexity: Measures the number of basic operations an algorithm performs as a function of input size n. Expressed using Big-O notation.
Common time complexities:
  O(1) = Constant Time = Accessing an element in an array
  O(n) = Linear Time = Traversing an array
  O(log n) = Logarithmic Time = Binary Search
  O(n log n) = Linearithmic Time = Merge sort, Quick sort
  O(n2) = Quadratic Time = Bubble sort

## Slide 68: Complexity Analysis of Algorithms
Best, Worst, and Average Case Complexity
  Best Case (Ω - Omega): Minimum time an algorithm takes for optimal input.
  Worst Case (O): Maximum time an algorithm takes for the worst input.
  Average Case (Θ - Theta): Expected runtime for random input.

## Slide 69: Complexity Analysis of Algorithms
2. Space Complexity: Measures the amount of extra memory an algorithm needs during execution.
3. Why Does Complexity Analysis Matter?
  Helps in selecting the best algorithm for a problem.
  Identifies bottlenecks and improves efficiency.
  Ensures scalability for large inputs

## Slide 70: Matrix-Chain Multiplication
A problem in which the goal is to find the most efficient way to multiply a sequence of matrices.
Conditions:
Suppose you have two matrices A and B with rows * columns are 5*4 and 4*3, if the first matrix (A)’s column (4) is equal to the second matrix(B)’s row (4), then we can multiply them.
  By following it, if A * B = C, then C’s dimension will be 5*3, which means row of A * column of B.
  So how many multiplications do we need to fill up the matrix C?
  Cost = 5*3*4 = 60 multiplications.
How many ways can we multiply some matrices?

## Slide 71: Matrix-Chain Multiplication
Suppose we have (A1 x A2) x (A3 x A4)
The tree would be:
Simple equation to take out the possible ways:
where n is the number of nodes.
= ( 2n! / n!n! ) / n+1

## Slide 72: Practice in class
What is the assembly language statement corresponding to this machine instruction?
00af8020hex
A somewhat complex statement contains the five variables f, g, h, i, and j:
f = (g + h) – (i + j); What might an Assembly compiler produce?
Show the IEEE 754 binary representation of the number –0.75 in single and double precision.

## Slide 73: The end